## Slide 1
DEFORESTATION DETECTION
A pixel-wise anomaly detection algorithm that will contribute in in monitoring and preventing deforestation

## Slide 2
  Prepare a timeseries of pixel values from the satellite imagery
  Implement version of Breaks For Additive Season and Trend (BFAST) method
  Visualize the results
CHALLENGE

## Slide 3
  interview_area_brazil.geojson
  Analyzed the data used folium
  file:///C:/Users/theon/Downloads/brazil_map.html
EXPLORING DATA

## Slide 4
  Used features_brazil.npy
  Shape of (72, 368, 420, 13)
    72 time steps
    368, 420 the height and width of the image
    13 number of channels
BRAZIL DATA

## Slide 5
  12 different bands of the satellite data and one quality band indicating the quality of the image
  B01, B02, B03, B04, B05, B06, B07, B08, B8A, B09, B11, B12, SCL
13 CHANNELS
https://docs.sentinel-hub.com/api/latest/data/sentinel-2-l2a/
https://sentiwiki.copernicus.eu/web/s2-applications

## Slide 6
index 0
index 1
index 71
......
13 channels

## Slide 7
Used RGB channel to visualize the images
B04 Red
B03 Green
B02 Blue

## Slide 9
  Used to identify burned areas and provide a measure of burn severity
  Ratio between the NIR (near infrared) and SWIR (shortwave infrared) values
  NBR = (NIR - SWIR) / (NIR + SWIR)
  NBR = (Band 4 – Band 7) / (Band 4 + Band 7)
NORMALIZED BURN RATIO (NBR)
https://www.usgs.gov/landsat-missions/landsat-normalized-burn-ratio

## Slide 10
  Normalized Burn Ratio or NBR returns values between -1 and 1.
  Positive NBR values indicates healthy green vegetation while while burnt vegetation will have a low value.

## Slide 11
  Considered a pixel with
    row_index = 160
    col_index = 215
VISUALIZING PIXEL TIMESERIES

## Slide 14
  Value started to decline over the years meaning the vegetation was becoming BURNT or BROWN vegetation or BARE SOIL
  A seasonality, the start of the year it is dry or brow vegetation but over the the months (mid year) it becomes greener.
  This shows a possiblity of rain as discussed in https://en.wikipedia.org/wiki/Climate_of_Brazil

## Slide 15
FITTING BFAST ALGO

## Slide 16
BFAST ALGO
  Uses additive season and trend model
  Two periods:
    History : Data acquired and analysed for stability
    Monitoring: New data acquired and analyse for disturbance
https://bfast.r-forge.r-project.org/Verbesselt+Zeileis+Herold-2012.pdf

## Slide 18
BFAST ALGO
  During monitoring phase uses moving sum (MOSUM) of residuals
  MOSUM has a sliding window h (h-hyperparameter )
  MOSUM process is close to zero if model remains stable
  MOSUM process deviates from zero if structural change occur
https://bfast.r-forge.r-project.org/Verbesselt+Zeileis+Herold-2012.pdf

## Slide 19
Case where
no break was detected

## Slide 20
The next slide contains an example for break
nbr_data[:, 0, 306]

## Slide 22
  NBR value on which break is detected: -0.668
  Date on which break is detected: 2022-07-01 00:00:00

## Slide 25
Started Monitoring from 2019 onwards

## Slide 26
Challenges
  Limited Data - model not able to fit
  Hyperparameters
  Labeled data to make deductions conclusive

## Slide 27
Future Approaches
  Additional information
    Looking into the soil minerals or texture
    Weather data
  Handling nan values
    Masking the value
    Temporal Interpolation

## Slide 28
THANK YOU